| MEMORANDUM FOR | JRI-Denton Operations ATTN: Mike McAvoy 113 South Bates Street Charleston AFB SC 29404 | 7 March 2006 |
| --- | --- | --- |

| FROM: | ASC/ENFC (ATTLA) 2530 Loop Road West Wright-Patterson AFB, OH 45433-7101 |  |
| --- | --- | --- |

SUBJECT: Air Transport Certification for a modified Blue Bird Bus (Your request 3 February 2006)

- The subject Bus (VIN 1BAAHCSH2MF04623Y) is identified to be a two-axle vehicle measuring approximately 426”L x 102”W x 130”H with a reported weight of 20,000 lbs.  The forward axle is rated at 11,340 lbs and the rear axle is rated at 17,000 lbs.

- The above items are herein approved for airlift in an AMC gained or operated USAF C-17 and C-5 prime mission cargo aircraft with the following comments:

- Shipper supplied approach shoring is required for loading (see attachment for recommendation).

- Tire pressure shall not exceed 100 psi for airlift.

- If the forward axle weight exceeds 9,070 lbs. or the rear axle exceeds 13,600 lbs shipper supplied sleeper shoring at least 10”L x 10”W (14”W under rear axle on C-17) and stacked to within ¼ inch of the frame in height is required under the frame near the heavy axle.

- The bus shall be secured to 3 G forward, 2 G up, and 1.5 G aft and laterally.  Restraint will be applied at the loadmaster’s discretion to suitable structure on the vehicle.  Axles & unsprung components of the running gear shall not be used for more than half the required restraint.  All items mounted or stowed within the vehicle must meet the restraint requirements in addition to a potential 4.5G download force.

- Any hazardous materials shall be prepared and packaged per AFMAN 24-204(I).  This memo is not to be considered as approval for shipment of hazardous materials, which must be granted separately.  The servicing aerial port can assist in this regard.

- The Shipper shall give a copy of this memo to the ATOC representative when the item is presented for airlift.  This memo shall be part of the official cargo manifest documentation package and will be briefed to the aircraft loadmaster prior to loading this item.  Point of contact is the undersigned at (937) 255-9639/DSN 785-9639.  Please refer to file number 2006.03.03

Eric Treadwell

Air Transportability Test Loading Agency

Attch: Recommended Shoring Dimensions

cc: HQ AMC/A37V

Minimum Recommended Shoring Dimensions for Modified Blue Bird Bus

Shoring requirements for other configurations are in the applicable aircraft loading manual.

C-17 Shoring

Pedestal Shoring “A” --none

Approach Shoring “B” 17” H x 24” W x 174” L

(14.5 feet long) 2 required

(shortest board should be 11”)

C-5 Aft Shoring (Aft Kneel)

Pedestal Shoring “A” --none

Approach Shoring “B” 18”H x 24”W x 180”L

(15 feet long) 2 required

(shortest board should be 11”)

C-5 Forward Shoring (Forward Kneel)

Pedestal Shoring “A” & “B”

“A”  --none

“B”  11”H x 15”W x 15”L  (4 each)

Approach Shoring “C” 17”H x 24”W x 174”L

(14.5 feet long) 2 required

(shortest board should be 11”)